Code reference

<switch 1 interrupt handler>
Checks if the USB is connected by checking the USB connection pin. If USB is connected, prompts the system to output all data from the EEPROM to

void blinkLED(uint8_t LEDnum)
Parameters: uint_8 LEDnum – LED number
Results: Causes the inputed LED number to blink

void toggleLED(uint8_t LEDnum)
Parameters: uint_8 LEDnum – LED number
Results: Causes the inputed LED number to toggle

boolean writeToEEPROM
Parameters: data to write
Results: Writes the given data to the EEPROM. If the EEPROM is full, writes no data
Return: True if data successfully written, false otherwise

void fetchFromEEPROM
Results: Fetches all data from the EEPROM

uint_16 readSensor(char sensorNumber)
Parameters: A character representing the sensor to read from
p: Potentiometer
x: Thermistor
l: Light
t: Temperature & Humidity (temperature)
h: Temperature & Humidity (humidity)
Return: A 12-bit ADC reading from the potentiometer

void powerSensor(char sensorNumber, boolean powervalue)
Parameters:
A character representing the sensor to read from
p: Potentiometer
x: Thermistor
l: Light
t: Temperature & Humidity (temperature)
h: Temperature & Humidity (humidity)
A boolean representing the desired power state
true: on
false: off