Code reference

<switch 1 interrupt handler>
Checks if the USB is connected by checking the USB connection pin. If USB is connected, prompts the system to output all data from the EEPROM to

void blinkLED(uint_8 LEDnum)
Parameters: uint_8 LEDnum – LED number
Results: Causes the inputed LED number to blink

void toggleLED(uint_8 LEDnum)
Parameters: uint_8 LEDnum – LED number
Results: Causes the inputed LED number to toggle

boolean writeToEEPROM
Parameters: data to write
Results: Writes the given data to the EEPROM. If the EEPROM is full, writes no data
Return: True if data successfully written, false otherwise

void fetchFromEEPROM
Results: Fetches all data from the EEPROM

uint_16 readPotentiometer
Return: A 12-bit ADC reading from the potentiometer

uint_16 readThermistor
Return: A 12-bit ADC reading from the thermistor

uint_16 readLight
Return: A 12-bit reading from the light sensor

uint_16 readTemperatrue
Return: A 12-bit temperature reading from the temperature & humidity sensor

uint_16 readHumidity
Return: A 12-bit humidity reading from the temperature & humidity sensor