Each I/O trace will be connected to two separate pins on the microcontroller. Each trace will have a 0Ω resistor between the sensor pin and the microcontroller pin, but one of these 0Ω resistors will be DNP. This will allow a different microcontroller pin to be used in the event that one fails.

The line to the voltage will also be populated with a 0Ω, to allow the entire module to be disconnected from power in the instance that a design error and/or circuit damage within the sensor module leads to a short.

If the 0Ω resistors have to be de-soldered, their pads can be used to solder a wire directly to another pin on the microcontroller.

Finally, the design includes 2 analogue sensors (a potentiometer which can be connected to some small mechanical device, and a thermistor), and 2 digital sensors (an ambient light sensor and a temperature/humidity sensor). Best case scenario, this means that the HAT is multi-faceted and can serve a variety of different research purposes. However, in the event of of component/design failure or inadequate component stock, the HAT will hopefully still have other functioning sensors and thus will still be useful. It is specifically useful that there are 2 different temperature sensors, given that our original examination of use cases for the HAT placed on a strong emphasis on the HAT’s ability to sense temperature.