Each I/O trace will be connected to two separate pins on the microcontroller. Each trace will have a 0Ω resistor between the sensor pin and the microcontroller pin, but one of these 0Ω resistors will be DNP. This will allow a different microcontroller pin to be used in the event that one fails. These connections are shown on the microcontroller schematic.

The l main power line will also be populated with a 0Ω, to allow the entire module to be disconnected from power in the instance that a design error and/or circuit damage within the sensor module leads to a short.

If the 0Ω resistors have to be de-soldered, their pads can be used to solder a wire directly to another pin on the microcontroller.

Finally, the design includes 2 analogue sensors (a potentiometer which can be connected to some small mechanical device, and a thermistor), and 2 digital sensors (an ambient light sensor and a temperature/humidity sensor). Best case scenario, this means that the HAT is multi-faceted and can serve a variety of different research purposes. However, in the event of of component/design failure or inadequate component stock, the HAT will hopefully still have other functioning sensors and thus will still be useful. It is specifically useful that there are 2 different temperature sensors, given that our original examination of use cases for the HAT placed on a strong emphasis on the HAT’s ability to sense temperature.

Temperature & humidity sensor: C2837688

What did you do in the past week?

- Added a temperature/humidity sensor to the sensor schematic
- Revamped net labelling system on schematics
- Error-checked and assisted other team members with the power and microcontroller submodules

What do you plan to do in the coming week?

- A bulk amount of the PCB design, given that I enjoy it and have had less work than the others so far
- A budget review to make sure we can actually afford all the sensors
- Any necessary final edits to the schematics

What might prevent you from doing things?

- Very busy next week (tests). Can mitigate with good time management
- Load shedding makes working difficult. Will plan around the load shedding schedule.
- Budget constraints might require some minor sensor submodule redesign. Will plan this in in case it is necessary.